# Introduction

Mark3 is a real-time development platform for AVR microcontrollers written using C++. It features a fully-featured RTOS kernel, device drivers, and middleware, as well as a suite of examples and unit tests.

Due to being written in C++ for AVR using the GCC toolchain, it also integrates directly into Arduino, without additional modifications to the source.
# Directory Layout

arduino	Scripts and staging directory for exporting Mark3 for Arduino
bootloader	Source and makefiles for the Mark3 Bootloader
build	Platform/variant/toolchain specific build configuration files
docs	PDF and HTML documentaiton
drivers	Device driver libraries
examples	Application code examples
fonts	Fonts converted from TTF to bitmapped, C++ library fonts
kernel	Main RTOS kernel code
services	Optional support libraries and middleware
stage	Directory where build artefacts are placed
tests	Unit testing framework

# Building the source

To build the source, the Mark3 build system requires the following:

avr-gcc toolchain
make support

On debian-based distributions, such as Ubuntu, the avr toolchain can be installed using:

apt-get install avr-libc gcc-avr

On Windows, the toolchain is provided as part of AVRStudio. Please see the “Build System” section of the docs for instructions on configuring the system on Windows.

Once a sane build environment has been created, the kernel, libraries, examples and tests can be built by running build.sh from the root directory. By default, Mark3 builds for the atmega328p target, although other supported targets can be configured through environment variables. See the base.mak makefile, and “Building the Kernel” in the docs for more information on configuring these variables.

# Supported targets

Currently, Mark3 supports the following parts:

atmega328p
atmega644
atmega1284p
atxmega256a3 (*experimental)

# Additional Documentation

Please see the doxygen documentation in the ./docs folder for more information. A lot of work has gone into documenting the project, and that's the best place to start if you have any questions. The code examples are fairly comprehensive (as are the unit tests), so these should be referenced as necessary. And of course, the source is very well-documented, so don't be afraid to browse through it.
# Contact

Email Funkenstein Software for any additional queries or comments:

funkenstein.sw@gmail.com

The official Google Code page for the project is located at:

http://code.google.com/p/mark3/